## Slide 1: dATA acquisition
Blake Rohde, Joel Tanzi, Michael Albert
Wireless Connectivity: Michael Tran
CAN-Bus Interfacing: Trey Zhong

## Slide 2
Wireless Modular Data Acquisition System
Project WiMDAS

## Slide 3: Project Features
Modular, abstracted design
  USB or Ethernet-connected devices/microcontrollers interface to external protocols
    E.g. CAN, SPI, I2C, Serial, GPIO, etc.
SD Card-based storage
Real-time web interface for live-race analysis
Utilities for exporting data into existing, mature data analysis products for post-race analysis
  E.g. GDA's GEMS, MoTeC's i2, etc.
Project WiMDAS

## Slide 4: Objectives Breakdown
Vehicle Host (V-Host)
  Intercept/capture all communications
    PCM-required (“primary”) sensors via CAN buses
    PCM output to sub-systems, debug messages
    “Secondary” sensors, e.g. GPS
  Relay all input wirelessly to R-Host
  Develop efficient storage, communication protocols
    Microcontroller-to-VHost data transmission
    Vhost-to-RHost wireless data transmission
    Data storage protocol
Remote Host (R-Host)
  Retrieve and capture/store all V-Host transmissions
  Host LAN/WiFi-accessable real-time web interface
    Preset and user-configurable panels
    Continuous, pause-able, zoom-able graphs for time-sensitive metrics
    Message panel for threshold alerts, debug messages
Project WiMDAS

## Slide 5: System Block Diagram
Project WiMDAS

## Slide 8: Hardware Breakdown
“ARM+Linux Device”
  Raspberry Pi
    700 MHz ARM11, 256 MB RAM
    10/100 Ethernet, USB
    Composite RCA & HDMI Video
  USB SD Card R/W’er
“CAN Interface Microcontroller”
  Arduino Mega2560
  SparkFun CAN-BUS Shield
“Microcontroller”
  Arduino Mega2560
“Wireless Module”
  Ubiquiti Networks airMAX Rocket M
    10/100 Ethernet interface, 100+ Mbps (12.5 MB/s)
Project WiMDAS
Source: Wikimedia (jwrodgers)

## Slide 9: Wireless Connectivity
Relay sensor data to ground station
Requirements
  At least 50 Mbit/s at >1 km range
  Manageable space and power footprint
Recommended modules
  Ubiquiti Networks airMAX Rocket M5
    10/100 Ethernet interface, up to 300 Mbit/s (37.5 MB/s)
    2.5 W typical power draw, 8 W max
    $80
  Ubquiti Networks Omni 5G-10 antenna
    Omnidirectional, 2x2 MIMO, 10 dBi gain
    0.68 kg, 10lb wind loading at 100 mph
    $110
Project WiMDAS

## Slide 10: Wireless Transfer Speeds
Available Tx power and required Rx power are dependent on desired transfer speeds
Faster transfer rates decrease available Tx power and require higher Rx power
Project WiMDAS
MCS Index | Data Rate (Mbit/s) | Tx Power (dBm) | Rx Power (dBm)
MCS10 | 90 | 27 | -90
MCS11 | 120 | 27 | -87
MCS12 | 180 | 26 | -84
MCS13 | 240 | 24 | -79
MCS14 | 270 | 22 | -78
MCS15 | 300 | 21 | -75

## Slide 11: Wireless Link Budget
Maximum 300 Mbit/sec probably not achievable
  Very little (3 dB) fade margin
90 or 120 Mbit/sec is achievable
  20-30 dB is a comfortable fade margin
Project WiMDAS
Tx power | 21 dBm
Tx antenna gain | 10 dBi
Tx mismatch | - 0.177 dB
Free space path loss (1 km) | - 106.4 dB
Atmospheric attenuation | Negligible at 1 km
Object fade | <3 dB with LOS
Polarization loss | <3 dB proper orientation
Rx antenna gain | 10 dBi
Rx mismatch | - 0.177 dB
Rx power | - 70 dBm

## Slide 12: Wireless Considerations
5 GHz vs. 2.4 GHz vs. 900 MHz
  Lower frequencies have increased range (effective ~6 dB for 2.4)
  Lower frequency antennas are larger, sometimes more expensive
  2.4 GHz has a higher noise floor (Wifi, cordless phones, microwaves)
Omnidirectional vs. Directional Antennas
  Tradeoff increased gain (range/speed) for directionality
  High quality directional antennas are more expensive, but the increased gain may allow the use of cheaper quality antennas and still maintain required range/power
Mounting Issues
  Proposed antenna exerts ~8lb drag force at 100 mph
  Can be reduced with non-metal, radio-transparent aerodynamic fairing or shell
  Antenna must be properly oriented (vertically) to avoid polarization loss
Project WiMDAS

## Slide 13: Antenna Dimensions
Project WiMDAS
Antenna
Antenna + Module

## Slide 14: Schedule – December 1, 2012
Vehicle Host (VHost) completed
  Auto-connect to USB-connected microcontrollers (DONE)
  Save data from USB-connected microcontrollers (DONE)
    Microcontroller-to-VHost protocol (DONE)
    VHost storage protocol (DONE)
  Extend to allow interface for Ethernet-connected devices
  Program “CAN-Interfacing Microcontroller”
  Program secondary-sensor microcontroller(s)
  Program steering wheel screen GUI application
    Will run on VHost, read parsed data from VHost core application via Unix Socket
Project WiMDAS

## Slide 15: Schedule – Remaining
January 1, 2012
  Wireless module & antenna testing completed
    Hardware testing
    Isolation testing
    Range testing
  Data converter utility
    Or MATLAB script(s) if commercial data analysis tools cannot be sourced
February 1, 2012
  Remote Host (RHost) completed
    Read data sent by VHost
    Save/replicate data
    Design and program real-time web interface
  Wireless integration
Free-time Bonuses
  Video stream
Project WiMDAS